| JOB SAFETY ANALYSIS | Job Task: Attaching a snow plow to a vehicle | Date: 9/1/2010 | New:9/1/2010 Revised |
| --- | --- | --- | --- |
|  | Title of Person Who Does Job: PUBLIC WORKS | Supervisor: JP | Analysis Performed By: KMB/ERJ |
| Organization: UWCHLAN TOWNSHIP | Location: TOWNSHIP COMPLEX | Department: PUBLIC WORKS | Reviewed By: RLR |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Ground crew to help position vehicle operator and visually line up plow frame to vehicle mount. | Crew members could be struck by vehicle. Vehicle could be damaged by striking plow | Crew members must notify operator of their positions. Operator must slowly position vehicle. |
| 2. Ground crew raises plow frame with a floor jack to align with frame on vehicle. | Back injuries Drop/crush injuries | Use of the jack prevents manually lifting plow. Keep clear of area beneath plow frame. |
| 3. Truck is pulled into place to lock(pin) plow frame to frame on vehicle | Crush/pinch hazards | Ground crew stands clear of area between plow and vehicle. Operator slowly approaches plow frame following direction of ground crew. |
| 4.After pins are connected, vehicle is placed in park and brake is set. | Crush/pinch hazards | Vehicle parking brake is set or vehicle is placed in park and shut off. |
| 5.Plow lift chains are hooked to plow hoist. | Lifting hazards | Use proper lifting techniques to lift chains. |
| 6. Hydraulic lines are attached to vehicle. | Splash/contact with hydraulic fluids | Ground crew to wear gloves and safety glasses. |
| 7. Plow operations are tested. | Plow could strike ground crew Plow could fall off vehicle | Ground crew stays away from plow and vehicle as tested. |