| JOB SAFETY ANALYSIS | Job Task: Attaching a Trailer to a Vehicle-Version 1 | Analysis Performed By: White Township |
| --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| Back tow vehicle up to trailer centering hitch under trailer tongue. | Damage equipment | Utilize two people - spotter to provide direction to driver |
| Lower trailer down onto hitch making sure to close hitch and lock with hitch pin. | Could lose trailer causing damage, injury or death | Verify hitch is locked and pinned |
| Make sure to move support on trailer tongue to highest position to prevent it from coming into contact with ground. | Equipment damage | Verify support is retracted to its highest position |
| Hook safety chains forming X pattern under tongue. Left chain on tongue to right side of hitch and right chain on tongue to left side of hitch. | Equipment damage, injury or death | Verify correct hookup and X pattern. Note: safety chain attachments are required to be clips (S hooks are no longer legal) |
| Plug in electrical plug for trailer lights. | Accident | Check connection |
| Do a pre-trip inspection checking lights, tires, load properly secured. | Malfunctioning equipment | Repair and/or report to Supervisor or Management immediately |