| JOB SAFETY ANALYSIS | Job Task: Attaching a Trailer to a Vehicle-Version 2 | Date: | Analysis Performed By: Uwchlan Township |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Check area between truck and trailer for obstructions. | Injuries to employee or damage to property | Visually check that area is clear Remove any obstructions |
| 2. Check mirrors on vehicle. | Driver may not be able to see when backing up to trailer | Adjust mirrors properly |
| 3. Turn off vehicle radio/stereo. | Inability to hear commands/warnings | Turn off radio |
| 4. Confirm with spotter (if available) that operator is going to back up trailer. Spotter should stand in a location where easily seen by the operator but also away from any pinch/crush points | Striking subject (s) who are assisting with attaching trailer Spotter being pinned between vehicle and trailer | Verbally confirm that spotter is prepared to assist with attaching trailer Spotter should stand off and to the left of the trailer tongue |
| 5. Place vehicle into reverse and slowly back up to trailer. If spotter is available, follow predetermined hand signals to back up to trailer. | Quick acceleration may exceed ability to control vehicle Miscommunication between operator and spotter may result in a inability to connect vehicle and trailer | Slowly apply the accelerator and prepare to apply brakes Operator and spotter must both understand signals and commands to guide the vehicle |
| 6. When vehicle and trailer are properly aligned, stop vehicle and apply parking brake. | Vehicle may move | Apply parking brake |
| 7. Securely attach trailer to vehicle and connect all appropriate safety chains and light/brake wires. | Trailer may become unhitched from vehicle during loading or transport Brakes may not work properly | Verify by sight and feel that trailer is secured to vehicle Pump vehicle brakes and listen for trailer brakes to engage |
| 8. Before moving vehicle and trailer, operator must be sure spotter and anyone assisting in connecting trailer is clear of vehicle/trailer. | Spotter or another assisting employee may be struck while moving the vehicle | Visually confirm that the area around the moving components is clear |