| JOB SAFETY ANALYSIS | Job Task: Attaching a Trailer to a Vehicle-Version 3 | Date: | New: Revised: Analysis Performed By: Conemaugh Twp MA |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Back in truck for proper hook up. | Individuals around moving vehicles/equipment. | Have an individual driver serving as a ground guide. |
| 2. Begin hook up procedure. | Pinch point or crushing injuries. | Insure penal hitch is open, positioned properly for safe hook up. Insure safety pin is properly installed in the penal hitch attaching it to the truck. |
| 3. Raise lifting jack and lower trailer onto the penal hitch. | Pinch point or crushing injuries. | Once trailer tongue is centered over the penal hitch ring, raise lifting jack. Lower trailer onto penal hitch. Insure hands/fingers are out of harms way. |
| 4. Hook up safety chains, electrical braking cable and electrical trailer lighting cable. | None observed. | Insure aforementioned connections are properly done. Close penal hitch and insure safety pin is properly inserted. |
| 5. Check to insure break lights and turn signals operate properly. | Could cause vehicle accident and personal injury. | Driver and assistant need to work as a team to check proper functions. |
| 6. Move Trailer to job site to begin necessary repairs/work items. | Could cause vehicle accident and personal injury | Driver and assistant follow all traffic/highway laws. |