| JOB SAFETY ANALYSIS | Job Task: Attaching a Plow to Vehicle | Date: 2/10/11 | Analysis Performed By: City of Meadville |
| --- | --- | --- | --- |

| SEQUENCE OF JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| --- | --- | --- |
| 1. Select proper vehicle for plow assembly. Assemble a 2-man crew. Clear assembly area of all debris. | Plow may not work properly. Injury could occur w/o crew to help. Employee/equipment may slip/fall. | Use proper equipment. Work w/others, not alone. Keep work area free of debris. |
| 2. Driver moves truck into position w/ help of crew. W/crew’s direction driver slowly moves truck to plow. | Employee could be pinched or run over. Equipment damage could occur. | Follow ground crew’s direction. Move vehicle slowly when positioning. |
| 3. When truck frame is close to plow frame, driver stops truck and sets parking brake. | Employee could be pinched or run over. | Set parking brake to ensure that ground crew will not be injured by unexpected movement of vehicle. |
| 4. Crew places floor jack under plow frame. Crew raises plow frame to heighth of truck frame. | Back injuries could occur. Pinch or crush injury could occur if plow drops. | Use floor jack – do not manually lift plow. |
| 5. Crew moves to safe position to direct driver toward plow after alignment of plow frame & truck frame is complete. | Employee could be pinched or run over. | Ground crew stands clear of area between plow & truck. Driver slowly moves vehicle toward plow frame being directed by his crew. |
| 6. Driver stops truck & sets parking brake & shuts engine off. | Employee could be pinched or run over. | Set parking brake to ensure that ground crew will not be injured by unexpected movement of vehicle. |
| 7. Crew installs plow pins & connects hydraulic hoses. Crew moves to safe position. | Employee could be pinched or run over. | Wear safety glasses and work gloves. |
| 8. Crew hooks up lift chain making sure it is not twisted. Crew moves to safe position. | Lifting injury could occur. | Use proper lifting techniques. |
| 9. Driver starts truck, checks to make sure that crew is away from plow. Driver checks plow by raising, lowering & turning it. | Employee could be pinched, crushed or hit by plow. Hose could be cut. Plow could fall off. | Ground crew must stay clear of plow testing area. |
| 10.Crew checks all lights and hydraulic oil level. Crew directs driver as he backs out of building. | Contact w/hydraulic fluid could occur. Employee could be hit or run over. Building or equipment damage could occur. | Check all lights. Check hydraulic fluid. Driver slowly moves vehicle under the direction of the ground crew. |