| JOB SAFETY ANALYSIS | Job Task: Bucket Truck Operation JSA No: WT-2010-1 | Date: 5/6/10 | New: Revised |
| --- | --- | --- | --- |
|  | Title of Person Who Does Job: All Authorized White Township Personnel | Supervisor: | Analysis Performed By: Ron Backus Brad Lowmaster |
| Organization: White Township | Location: Various | Department: All | Reviewed By: Milt Lady Chris Anderson |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Employees enter bucket truck. | Emergency or accident occurs. | Need to have one person as operator and one as spotter to watch for hazards and assist operator. |
| 2. Park on solid, level surface. | Rollover | Read level meter on dash. Adjust truck as necessary. |
| 3. Turn on generator switch. | No power. |  |
| 4. Chock wheels. | Truck movement. | Place chocks at front and rear of the same rear wheel. |
| 5. Prepare for bucket operation. | Operator safety. | Put on PPE (harness, hard hat, gloves, sound protection). |
| 6. After occupying bucket, press generator start button. | No power |  |
| 7. Operate switches to move boom. | Injury or Death | Be aware of surroundings and environment. |
| 8. Obtain elevation/location of work. | Accidental bucket movement. | Push stop button to kill power to boom. |
| 9. In case of emergency operation | Bucket operator accident | May operate boom from right rear compartment of truck. |
| 10. Return boom to closed position. | Operator injury & equipment damage | Make sure boom is in final position – completely retracted and in cradle. |