| JOB SAFETY ANALYSIS | Job Task: Changing a Street Sweeper Broom | Date: | Analysis Performed By: City of Lebanon |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Lower main broom. | Removing excessive weight |  |
| 2. Remove bolts from arm that runs bearings on shaft. | None observed | Use ¾” socket wrench Wear gloves Wear safety glasses |
| 3. Pull broom out from under sweeper. | Back strain | Have partner assist Wear gloves Wear safety glasses |
| 4. Remove bolts (5 per side) and pull out shaft. | None observed | Wear gloves Wear safety glasses |
| 5. Install new broom. | None observed | Ensure bolts are tightened |