| JOB SAFETY ANALYSIS | Job Task: Changing Blades on a Lawnmower | Date: | Analysis Performed By: City of Lebanon |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Place the mower onto car ramp or jack. | Mower could roll off ramp | Chock the wheels Ensure mower is in “lock” position Remove key from ignition Rinse off mower |
| 2. Select tools to remove blade(s). | None observed | Wear gloves and face shield |
| 3. Remove blade(s). | Blade(s) could fall onto employee Debris in eye | Wear ANSI approved eye and face protection Wear gloves |
| 4. Install new blade(s) | Blade(s) could fall onto employee Debris in eye | Wear ANSI approved eye and face protection Ensure blade(s) is installed properly Wear gloves |
| 5. Lower mower and remove from car ramp or jack. | None observed | None |