| JOB SAFETY ANALYSIS | Job Task: Daily Airpack Check | Date: 12/15/10 | Analysis Performed By: City of Meadville |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Disconnect bottle from air pack. | If cracked of broken could cause air leak. Life safety | Check white o-ring on airpack. Change o-ring if damaged. |
| 2. Reconnect bottle to airpack. | Could wear threads if over tighten. Life safety | Make sure you tighten hand tight. |
| 3. Turn air on at bottle. | Could have false reading at airpack gauge. Life safety | Make sure air gauge at bottle matches air gauge on airpack. Within 10 % |
| 4. Check all straps. | Could become dislodged from firefighter. Life safety | Inspect for discoloration, rips, or excessive wear. |
| 5. Check air bottle bracket. | Could separate from pack. Life safety | Make sure bottle is locked and secured to air pack. |
| 6. Check waist strap and buckle. | Difficult to properly fit if worn or broken. Life safety | Make sure strap and buckle are not worn or broken. |
| 7. Check chest strap and buckle. | Difficult to properly fit if worn or broken. Life safety | Make sure strap and buckle are not worn or broken. |
| 8. Bleed air from bottle via bypass valve. | Life safety | Make sure all alarms sound including quarter air alarm. |
| 9. Pack ready for service. |  |  |