| JOB SAFETY ANALYSIS | Job Task: Driving a Snow Plow | Date: | Analysis Performed By: Borough of Derry |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Drive to storage area and position truck to plow. | Positioning incorrectly injuring employee | Always utilize two people Second person should guide driver to plow standing back in a safe zone |
| 2. Insert bottom pins. | Slip trip or fall due to ice or snow | Work as a two person team utilizing safe bending procedures |
| 3. Lock pins. | Hammer can slip causing injury to hand or finger | Pre-line up pins and work together balancing while locking pins in place |
| 4. Connect hydraulics and power source (electric). | Pinch hazard hydraulic oil spill | Wear safety glasses Take time connecting without interruption |
| 5. Test plow. | Equipment breakage or disconnection of plow causing employee injury | Second person should be in safe area while driver test plow making sure it works properly |