| JOB SAFETY ANALYSIS | Job Task: Driving a Zamboni | Date: 6/10/10 | New: Revised |
| --- | --- | --- | --- |
|  | Title of Person Who Does Job: | Supervisor: Frank Lehman | Analysis Performed By: City of Greensburg |
| Organization: City of Greensburg | Location: Kirk S. Nevin Ice Arena | Department: Recreation | Reviewed By: |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Unplug Zamboni from 2600 Volt Battery charger. | Dropping plug in water or putting finger in plug receptacle. | Wrap cord around arm and shoulder until it is hung up and wear gloves. |
| 2. Turn Zamboni on and raise the conditioner up and off of support boards/plates. | Hitting a person with the conditioner, raising it or dropping it on foot or hand. | Look to make sure area is clear of people. |
| 3. Put Zamboni in reverse and slowly back Zamboni through doors and onto the ice. | Hitting a person or the Zamboni doors on the way onto the ice. | Look for people or objects in your way and make sure Zamboni doors are open fully. |
| 4. Put Zamboni in operating forward position and lower conditioner. | Hitting patrons on ice, dropping conditioner on foot. | Make sure ice surface is clear of skaters, if it is not, beep horn. |
| 5. Turn on the hot & cold water. Turn on augers and adjust Zamboni blade accordingly. | Hitting patrons, getting hand, foot, or clothing in auger. Dropping the cutting blade. | Pay attention to your surroundings. Keep objects away from augers and grooming blade. |
| 6. Groom ice surface, cutting; using cold wash water and warm ice, making water. | Hitting boards, glass, hockey nets, open doors, pucks, and patrons. | Be aware of your surroundings. |
| 7. When ice surface is completely groomed, prepare to exit through doors back into garage. | Hitting people, doors, kickplate, or garage floor. | Make sure doors are still open and clear of people or objects. |
| 8. Turn off hot & cold water, turn off augers and as you approach doors, raise conditioner and blade. | Not raising conditioner & blade before exiting ice surface into the garage. | Give yourself plenty of time to do all shut down procedures before reaching entrance to garage. |
| 9. Pull Zamboni into dump tank & parking area, raising & dumping snow, placing prop stick under tank. | Hitting people or things; dumping snow on someone. | Being aware of your surroundings, dumping snow into tank and parking properly. |
| 10. Lower conditioner down onto support boards/plates and turn the Zamboni off, take out key. | Dropping conditioner w/blade onto a person’s foot, and leaving key in machine. | Look behind you for people or things and taking key out of ignition in case of unwanted recharging or if an unauthorized driver appears. |