| JOB SAFETY ANALYSIS | Job Task: Emptying a Roll Off Container | Date | Analysis Performed By: Northern Tier SWA |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Back truck up to container. | Pedestrians, traffic, limited space Overhead wires and tree limbs. | Block off oncoming traffic. Remove obstacles from working area. Use extended side mirrors to back up Engage emergency brake and put truck in neutral. |
| 2. Using the hydraulic lever, fully raise the boom. | Overhead wires and tree limbs. Pinch hand and/or fingers Persons or objects struck by swinging cable | Be aware of surroundings. Attach winching cable to the container. |
| 3. Lift container onto the truck using the hydraulic lever. | Winching cable could snap. Truck could become unstable if container or booms are moved too rapidly. | Be aware of surroundings. Lower boom slowly so it is level with the container once the container is slightly lifted onto the truck for stabilization. |
| 4. Lowering the boom. | Truck could become unstable if container or booms are moved too rapidly | Lower boom slowly. |
| 5. Tarping container using “Auto Tarp” lever. | Pinch hand and/or fingers | Level off contents in the container to prepare for tarping. Secure tarp with extra bungee cords. |