| JOB SAFETY ANALYSIS | Job Task: Fuel Pump Operation & Spill Clean-Up | Date: | Analysis Performed By: Uwchlan Township |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Shut off vehicle at fuel pump. | Vehicle movement while unattended Ignition source(s) | Place in park Shut of vehicle ignition |
| 2. Remove vehicle fuel cap. | Sudden release of fuel vapors | Slowly remove fuel cap |
| 3. Insert nozzle into fill line. | Static charge could ignite fuel vapors | Touch vehicle body to eliminate any static charge before dispensing fuel |
| 4. Stop pumping fuel when nozzle clicks off. | Overflow/spill of fuel | Do not top off vehicle fuel tanks |
| 5. Shut off pump and replace nozzle. | Damage to nozzle or hose | Remove before starting vehicle |
| 6. If any fuel is spilled |  |  |
| 7. Verify all ignition sources are eliminated. | Fire | Be sure vehicle is not running, no one is smoking in the vicinity of the spill. Do not use cell phone in area of spill |
| 8. Use the materials provided in the spill kit located next to the fuel pumps to contain/clean-up the fuel spill. | Ignition of fuel/fire Ground/waterway contamination | Use oil dry to completely cover the fuel spill If spill is spreading to any storm drains, use provided boom pads to block/divert spill |
| 9. Sweep up all oil dry when spill has been absorbed. | Slip or fall hazard on loose materials | Place used oil dry in collection barrel |
| 10. If spill exceeds clean up materials provided, contact department supervisor and notify 911. | Extensive ground or water contamination | Contact additional resources immediately |