| Pull equipment next to proper side of fueling tanks – gas or diesel side – so the hose will reach fuel cap properly. | Gas spill due to overextending hose | Park within 2-5 ft of pump |
| --- | --- | --- |
| Shut down equipment. | Fire due to sparks | Install signage typical of gas station |
| Do not fill gas cans that are sitting on a truck bed liner. | Fire due to sparking if not grounded | Set gas cans on ground |
| Verify hose nozzle handle is NOT locked open and pump switch on tank is OFF. | Unattended fuel leak | Signage |
| Go inside building and turn pump timer on. |  |  |
| Return to tanks, remove fuel cap from equipment. |  |  |
| Place hose nozzle in equipment filler tube hole. | Fuel leak onto ground and/or fire due to malfunction | Operator to do first before turning pump switch on |
| Flip on on/off switch. |  |  |
| Pull handle on fuel hose to begin fueling. |  |  |
| Standby the equipment until fuel tank is full. | Fire hazard may exist due to spark caused by static | Operator is NOT to get in or out of vehicle |
| Release handle on hose nozzle and turn off pump switch at tank. | Fuel leak onto ground when returning nozzle to tank holder | Keep nozzle in equipment tank or gas can filler tube and verify both switches are off. |

| Pull trigger on hose to release pressure | Fuel leak onto ground when returning nozzle to tank holder | Operator to keep nozzle in equipment filler tube |
| --- | --- | --- |
| Return hose and nozzle to tank holder | Drive off and damage hose and/or nozzle |  |
| Place fuel cap back on vehicle | Fuel vapors | Operator to make sure cap is tightly closed (click) |
| Problems or hazards | Malfunction causing leak or fire | Report to Supervisor or Management immediately |
| In case of emergency or malfunction activate kill switch at tank | Fire or fuel leak | Install kill switch at tank |

Adopted: May 12, 2009