| JOB SAFETY ANALYSIS | Job Task: Inflating a Vehicle Tire | Date:9/1/2010 | New:9/1/2010 Revised |
| --- | --- | --- | --- |
|  | Title of Person Who Does Job: PUBLIC WORKS, FIRE, EMS | Supervisor: DH | Analysis Performed By: SW |
| Organization: UWCHLAN TOWNSHIP | Location: PUBLIC WORKS, FIRE, EMS | Department: SAME | Reviewed By: RLR |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1.Place vehicle on flat surface and chock wheels and/or set brake. | Injury due to moving vehicle | Utilize all available devices to prevent vehicle movement: brakes, wheel chocks, etc. |
| 2. Wear proper eye protection and clothing. | Debris from high-pressure air Injury potential from tire or hose failure | Wear eye protection, gloves as necessary. |
| 3. Make sure tire is cold. | Hot tire can be easily overinflated | Only fill tires when cold. |
| 4.Check recommended and maximum inflation pressures. | Over-inflation can lead to potential failure | Only inflate tires to recommended pressure and never exceed maximum pressure. |
| 5.Check connections and hoses on inflation source | Hose or hardware failure can cause injury | Check over hoses and fittings. |
| 6. Remove valve stem cap and check valve for damage. | Valve stem failure could cause injury | Inspect valve stem when removing cap. Do not inflate a tire with damaged stem. |
| 7. Stand away from tire. | Failure of tire, valve stem, or inflation components can cause injury | Stand to the side of the tire to minimize chance of being struck by debris. |
| 8. Inflate tire slowly. | Over-inflation can lead to potential failure | Inflate in small increments and check pressure in tire regularly with an accurate gauge. |
| 9. Replace valve stem cap and place inflation equipment in proper location. | Minimize chance for damage to valve stem Equipment not stored in proper locations can cause injury | Keep all valve stem caps in place. Return all equipment to designated locations. |