| JOB SAFETY ANALYSIS | Job Task: Jack Hammer Operations | Date: | Analysis Performed By: Penn Township |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Lift jackhammer from compartment inside of compressor. | Lower back, arm, and shoulder strain Pinched hand on side of compartment | 2 people needed to lift jackhammer Use lighter jackhammer 60 lbs instead of 90lbs Use optional way of storing jackhammer |
| 2.Carry jackhammer over to designated start point. | Back and arm strain Possible hernia | Use lighter jackhammer if possible Have 2 people to carry jackhammer |
| 3. Connect hoses to hammer and compressor. | Pinched finger when connecting hoses | Wear gloves when connecting hoses to compressor |
| 4. Position jackhammer at starting point. Start compressor and squeeze trigger to begin. | Possible hearing loss or particles in eye Jackhammer hitting feet | Wearing ear plugs and safety glasses at all times Position feet apart keeping a safe distance from blade of hammer |
| 5. Shut off compressor, bleed air from lines, disconnect hoses, and put jackhammer back in compartment. | Stay clear of moving parts on motor Dust blown into eyes Pinched finger Lower back, arm, and shoulder strain | Wear safety glasses and gloves Use 2 people to carry jackhammer Backup to compartment |