| JOB SAFETY ANALYSIS | Job Task: Jetter Use | Date: 2011 | Analysis Performed By: Berwick Borough |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Establish a safe work area | Being struck by a motor vehicle Potential damage to a passersby Tripping Injury to coworker | Place “Road Work Ahead” signs and flaggers at a reasonable distance from actual place of work. Wear fluorescent t-shirts and Reflective vests Place barricades around drywell. Inspect the area for any objects that may trip or a pose a threat to the operator All non-operators should remain at a safe distance from work area Maintain that all hoses are protected from being run over and crushed by vehicles |
| 2. Personal safety | Could be struck in eye by flying debris Could be a hazard to potential hearing loss Could lose grip on nozzle and place others in harm Could inhale potentially hazardous material Could slip and fall | Once safe area has been established and secured, the worker should place eye protection, ear protection, hand protection, mouth protection, gloves and proper footwear; respiratory protection and other PPE in appropriate places. |
| 3. Inspection of Equipment | Malfunctions and failure to start Blown lines High pressure could cause bodily harm | Before the worker begins work, an inspection of the Jetter should include the following: lubricating oil, water, hydraulic fluid, and fuel levels; condition of: guards, shields, and safety interlocks; filters and strainers; engine stop devices are clearly labeled and work; all throttle cables. Also, all hoses should be inspected to ensure that correct pressure rating and size is selected; ensure that there is no apparent structural damage, corroded or broken wires, bulging, kinking, or cuts; check all end fittings and couplings are in good order and of the correct pressure rating for the unit. |
| 4. Using High Pressure Hose | Severe bodily injury from high pressure water Flying debris Injury to another worker | Be alert and attentive. Point the high pressure nozzle at the drywell only and not in the direction of other workers. Co-workers shall stay at least 8 feet away from the drywell while high-pressure water is in use When co-workers are working in the drywell area, the safety shut-off shall be engaged on the high-pressure hose. |