| JOB SAFETY ANALYSIS | Job Task: Operating a Belt Sander | Date: 1/28/11 | Analysis Performed By: City of Titusville |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Turn on Power To Unit | Flying Debris / Objects | Wear Safety Glasses Work Area Clear of Debris / Objects Make Sure Guards in Place |
| 2. | Muscle Strain | Proper Body Positioning Avoid Twisting Firm Foot Placement |
| 3. Align Material & Make Contact | Flying dust / Objects | Secure Handle of Object, Firm Grip Wear Gloves & Appropriate PPE |
| 4. Maintain Proper Contact Pressure With Belt & Object | Flying Object / Debris | Apply Adequate contact pressure to avoid having the held object come loose from grip and slow belt |
|  | Contact with moving objects /Belt | Wear Proper PPE (Gloves / Eye & Face Protection) Do Not Wear Loose Fitting Clothing |
| 5. Shut Down Machine | Flying Debris | Remove object from belt Clear work from table Power Down unit with Appropriate Control |
| 6. Clean up & Housekeeping | Flying Debris Coming in contact with | Make sure Unit is still & at a zero energy state Clear debris from work area and peripheral floor surface area |