| JOB SAFETY ANALYSIS | Job Task: Operating a Radial Saw | Date: 1/28/11 | Analysis Performed By: City of Titusville |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION OR PROCEDURE |
| 1. Remove all jewelry. Secure loose clothing. Wear a hair net, if need be | Caught in, Entanglement | Do not wear jewelry, loose fitting clothing, and tie up and secure hair if need be, when operating a radial saw. |
| 2. Obtain Proper PPE. Clear face shield, Z97.1 safety glasses with side shields Approved respirator if needed | Struck by, Inhalation | Always wear adequate and approved PPE while operating the radial saw. |
| 3. Inspect work area around saw | Slip, Trip, Fall | Always do a walk around of the work area to ensure there are no debris and lighting is adequate |
| 4. Inspect the saw : *Stability of table *Electrical power source * Saw blade * Guards | Struck by, laceration, electrical shock | Bring the saw to a Zero Energy point by performing lock out / tag out procedures prior to inspection. Once a t a zero energy state, performing the following checks: * Make sure that all guards are in place an operable * Check the saw blade to ensure it is in good shape. Check for missing teeth, cracks, and make sure it has the appropriate RPM rating. Make sure the blade in secure in its mount. *Check the electric power source to include the switch, power cord, and receptacle. * Supply energy to the saw once inspection is completed. |