| JOB SAFETY ANALYSIS | Job Task: Restarting a Motor | Date: | Analysis Performed By: Borough of Pottstown |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Turn breaker to complete off position. | Sprain wrist | Use fluid motion to pull handle |
| 2. Turn breaker to complete off position. | Sprain wrist Electrical flash | Use fluid motion to pull handle Wear eye protection and non flammable clothes |
| 3. Push the reset button for the motor controller. | None | None |
| 4. Turn the motor on at the switch, VFD, or remotely. | Electrical flash at the controller or at the motor | Wear eye protection and non flammable clothes |
| 5. If the breaker or the motor controller trips off again DO NOT RESET IT call the electrician there are bigger problems. | Turning the motor on repeatedly could damage the motor or cause harm or death to anyone in the area | Do not reset or turn the motor on again after it trips off |