| JOB SAFETY ANALYSIS | Job Task: Using an Extension Ladder | Date: | Analysis Performed By: Borough of Derry |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION |
| 1. Remove roof ladder from truck. | Lifting incorrectly causing back injury | Two person operation work as set aside team lifting vertically the horizontally using proper lift methods |
| 2. Remove 24ft ext ladder from truck. | Lifting incorrectly causing back injury | Two person operation work as set aside team lifting vertically the horizontally using proper lift methods |
| 3. Carry ladder to site needed. | trip fall or strain | Work as team Lead man directs movement |
| 4. Raise ladder/extend ladder. | Slip trip and fall | Secure footing and lifting stance checking for overhead hazards Lift in sequence with first person raising second person securing bottom of ladder |
| 5. Secure ladder to 75 degree angle at top with Halyard. | Falling backwards/off ladder | Insure 75 degree angle with body check Secure bottom ladder |