| JOB SAFETY ANALYSIS | Job Task: Apply spray insecticide on Golf Course Greens. | Date: June 29, 2012 | Analysis Performed By: East Stroudsburg (Golf Course Maintenance Staff) |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. Requires Pesticide Applicator License. | Fines and penalties for improper use. | Obtain necessary credits to maintain license from PA Agriculture Dept. |
| 2. Put on PPE (Personal Protective Equipment). |  | Wear long-sleeve shirt and pants; use Respirator when handling or applying the chemical. |
| 3. Get insecticide from storage area. | Dropping container, causing material to spill. | Handle cautiously, and read label thoroughly. Check temperature, humidity, and barometric pressure. |
| 4. Place water into tank mounted on Truckster. | Spilling water and slipping/falling. | Fill 150 gal. tank (but not completely, allow for chemical mixing). |
| 5. Add insecticide into tank. | Coming into contact with insecticide. | Mix the insecticide thoroughly in tank, at the specified mix rate. |
| 6. Travel to golf green(s) to be applied on. | Overturning the Truckster. | Drive carefully and stay alert. |
| 7. Determine if conditions at site permit the application to be done safely. |  | Check wind speed, and that no one else is downwind. |
| 8. Apply insecticide to green. | Inhaling or coming into contact with the insecticide. | Spray evenly over the entire green; don’t overapply. |
| 9. Return to Maintenance Building and Cleanup afterwards. | Overturning the Truckster. Coming into contact with the insecticide. | Remove PPE and store properly. Clean and store equipment properly. |
| 10. Record usage. |  | Write in logbook date, times, name of chemical applied, amount used. |