| JOB SAFETY ANALYSIS | Job Task: Care and Maintenance of Chainsaw Chaps | Date: June 2012 | Analysis Performed By: Borough of Kennett Square |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. Inspection for tears, rips or petroleum contamination. | Reduced protection. | Inspect chaps for any tears, rips or petroleum contamination. Clean or repair chaps as required. |
| 2. Cleaning | Break down of protective Kevlar, increased fire hazard. | Use citrus-based cleanser to clean contaminants from chaps to protect Kevlar. |
| 3. Storage | Improper cleaning and storage may cause mold and other contaminants to break down the protective properties of Kevlar | Store chaps when ot in use in a clean, dry environment away from UV rays and mold that may fade and deteriorate the materials. |
| 4. Wear | Improper positioning may not properly protect the worker. | Ensure proper size and fit. Follow manufacturer’s instructions for proper use. |
| 5. Repairs | May result in reduction of protective properties of chaps, severe injury could occur if used as chain stop. | Follow manufacturer’s specifications for repairs to tears and rips. |
| 6. |  |  |
| 7. |  |  |
| 8. |  |  |
| 9. |  |  |