| JOB SAFETY ANALYSIS | Job Task: Care and Maintenance of a Hard Hat | Date: June 2012 | Analysis Performed By: Borough of Kennett Square |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. Inspection of the Shell | Failure of the hat shell | Inspect the shell for cracks, nicks, dents or any damage caused by impact, abrasions or rough treatment. Check for any brittleness, fading or chalky appearance. Remove any hats from service that show any of these conditions. |
| 2. Inspection of the Suspension | Hat falling off, shell too close to head | Inspect the suspension for frayed or cut straps, or for cuts or tears. All keys should fit tightly into their respective key slots. Remove from service any hats whose suspension exhibits any of these conditions. |
| 3. Storage | Brittleness and deterioration of the shell | Store the hat when not in use in a clean, dry environment away from UV rays that may fade and deteriorate the materials. |
| 4. Wear | Improper positioning may not properly protect the worker | Wear all hats with the brim facing forward, as this is the position in which it was tested to comply with ANSI certification. Do not place any items between the suspension and the shell. |
| 5. Adornments | May conduct electricity to the interior of the hat. | Place stickers a minimum of ¾” from the edge of the helmet. Monitor the reaction of the shell to any chemicals used in sticker adhesives. |
| 6. Field testing | May result in injury or death | Compress the shell inwards from both sides 1” then release without dropping the shell. If the hat does not return to its original shape or cracks from brittleness, replace immediately. |
| 7. |  |  |
| 8. |  |  |
| 9. |  |  |