| JOB SAFETY ANALYSIS | Job Task: Changing Tire on Public Works Truck | Date: June 2012 | Analysis Performed By: Derry Borough |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. Park Truck on Flat Surface using Emergency Brake | Uneven surface could create a malfunctioning jack | Use jack stands for stability in case floor jack would move |
| 2. Block tires from moving utilizing blocking devices | Vehicle could move when jacking up the car | Always block Tires for Safety |
| 3. Jack up Frame securing position | Truck could fall if jack falters or releases | Utilize all safety precautions with jack stands and blocking devices |
| 4. Inspect Footwear | Deformed safety toes or damaged boots can compromise feet safety | Replacement of boots |
| 5. Remove lug nuts and tire and replace tire securing lug nuts | Tire not evenly mounted could create a hazard | Tighten and secure Lug nuts in staggered sequence to be sure they are balanced Wear safety glasses when using air tool |
| 6. Retighten lug nuts after tire is back on ground and check air pressure | Loose lug nuts could cause tire to come off when operating vehicle. | Re-check lug nuts and balance of tire once tire is repositioned back on flat surface. |