| JOB SAFETY ANALYSIS | Job Task: Clearing Jam in Salt Spreader Auger | Date: June 2012 | Analysis Performed By: Ligonier Township |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. It is the responsibility of the truck operator to first park in an area where traffic can see the vehicle from both directions. | Being Struck by passing motorists | Safety glasses, safety gloves |
| 2. If spreader does not have an emergency disconnect on the auger drive, it will be necessary to take the power take off out of gear or turn the engine off. | Entanglement in Auger | Safety glasses, safety gloves |
| 3. Next, lower the bottom tray of your spreader, allowing the auger material to fall to the ground. This can be a considerable amount depending how much material is against the tailgate. | Material in eyes, Entanglement in auger, being struck by passing motorists | Safety glasses, safety gloves |
| 4. Allowing this material to exit should give the operator a visual as to what is jamming the auger. Most jams are generally lumps, rocks or roots that can be easily removed with a shovel, hammer or bar once the auger is visible. | Material in eyes, Entanglement in auger, being struck by passing motorists | Safety glasses, safety gloves |
| 5. Once the auger is clear, the lower pan can be reinstalled and locked in place. If there is not a large amount of material on the ground, it can easily be shoveled back onto the truck bed. | Material in eyes, Entanglement in auger, being struck by passing motorists | Safety glasses, safety gloves |
| 6. If a large amount of material is left on the roadway it may be necessary to either call for a machine or simply plow this material off the edge of road until you can come back and gather it up. | Material in eyes, Entanglement in auger, being struck by passing motorists | Safety glasses, safety gloves |
| 7. As designs can change depending on the manufacturer, some steps may need to be changed depending on the unit. | Material in eyes, Entanglement in auger, being struck by passing motorists | Safety glasses, safety gloves |