| JOB SAFETY ANALYSIS | Job Task: How to Operate a Line Painting Machine | Date: June 2012 | Analysis Performed By: City of Greensburg |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. Daily Procedure for utilization of line painting machine | Cleared work area and proper safety controls in place for traffic before machine operates. Employees use their safety glasses, vest and work boots while operating equipment. | Prepare the work site by clearing the road of debris |
| 2. |  | Place proper work zone equipment such as safety cones, signage and vehicle placement in area of work. |
| 3. |  | Prepare line painting machine by checking parts to make sure they work properly. Check gas & oil levels in motor. |
| 4. |  | Choose paint; mix in strainer, place paint on machine. Install strainer and tips to the paint gun. Start motor, engage pump switch and set proper pressure. Make sure pump is circulating. Switch to paint mode. |
| 5. |  | Place machine in proper location to paint line. Set the line machine lock (for straightness) |
| 6. |  | Spray Line…If satisfied with line, disengage pump & switch to circulate mode. |
| 7. |  | Return equipment to shop via trailer transport for machine clean up. |
| 8. |  | Remove paint which is leftover – seal lid to paint – remove strainer tips and clean in hot water. Install 5 gallon bucket of water on machine to clean out hoses and filters. |
| 9. |  | After all residual paint is dissolved, idle down machine, and shut pump switch pressure off. Shut motor off. Place machine for storage until next use. Lubricate pump as necessary. |