| JOB SAFETY ANALYSIS | Job Task: Performing routine maintenance on parking meter | Date: June 29, 2012 | Analysis Performed By: East Stroudsburg (Parking Enforcement Officers) |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| Determine if meter housing is cloudy or cracked. | None, really. | Identify if need to replace single, or double housing. |
| 2. Bring the necessary housing(s) to replace with. | Tripping or falling while getting at meter. | Carry spare housings and tools in bag for safe transit. |
| 3. Remove bolt holding housing(s) on post. | Having housing fall on hand or other part of body. | Using rachet, loosen bolt and lift off old housing(s). |
| 4. Remove coin cup to get at meter mechanism and housing. | Getting fingers jammed, or pinched or having metal door fall on foot. | Open cash door and remove coin cup, set aside without dropping. Remove meter mechanism. |
| 5. Replace the housing with new one. | Letting it slip out of hand and hurting yourself. | Insert new housing into meter cavity. |
| 6. Check if mounted properly and securely. | Getting fingers jammed, or pinched. | Check and clean inside of meter cavity as necessary. |
| 7. Reinstall coin cup and meter mechanism. | Getting fingers jammed, or pinched. | Insert meter mechanism and emptied coin cup. |
| 8. Reinstall bolt holding housing(s) on post. | Dropping or letting rachet hit body. | Using rachet, tighten bolt firmly. Move on to next meter. |
| 9. |  |  |