| JOB SAFETY ANALYSIS | Job Task: Power Wash Instructions – Step by Step | Date: June 2012 | Analysis Performed By: Hellam Township |
| --- | --- | --- | --- |
| SEQUENCE OF BASIC JOB STEPS | POTENTIAL HAZARDS | RECOMMENDED ACTION/PROCEDURE |
| 1. The power washer is located between the 1st & 2nd garage doors from the south side of the building. It is yellow in color. |  |  |
| 2. The garden & high pressure hoses that are needed are hanging above the power washer. |  |  |
| 3. Hook the garden hose up to the spigot. The spigot is located directly behind the power washer and is red in color. Firmly grasp the female end of the garden hose and screw it on clockwise to the male end of the spigot until tight. |  |  |
| 4. Firmly grasp the male end of the garden hose and insert it into the female end of the power washer. The female end is located on the south side of the power washer approximately 3” from the floor. |  |  |
| 5. Firmly grasp the male end of the high pressure hose and hook it up to the female end of the pressure washer which is located beside where the garden hose is attached to the power washer. |  |  |
| 6. Firmly grasp the female end of the high pressure hose and insert the male fitting on the spraying wand. |  |  |
| 7. Select the appropriate nozzle for the application and insert it into the end of the spraying wand. |  |  |
| 8. Firmly grasp the handle of the spigot and pull upwards to turn it on. |  |  |
| 9. Go to the west side of the power washer to turn it on – turn the knob 1 click to the right if job requires cold and 2 clicks to the right if it requires hot water. |  |  |
| 10. Firmly grasp the spraying wand and point it in a safe direction. | Injury to people | Point to object you are washing and be sure nobody is in path between you and object. |
| 11. Keep the end of the spraying wand approximately 12” away from what you are washing. | Damage to paint. | Keeping proper distance from object being sprayed |
| 12. Squeeze the handle on the spraying wand. | Damage to paint. | Keeping proper distance from object being sprayed |
| 13. Move wand side to side and up and down until item you are washing is clean. | Damage to paint. | Keeping proper distance from object being sprayed |